## Slide 2
Background: Hard to write fast code for programmable substrates

## Slide 3
Solution: Use program synthesis to autogenerate fast code

## Slide 4
int spec(int x) {
return x*5;
}
int sketch1(int x) implements spec {
return x << ??(2) + x;
}
int sketch2(int x) implements spec {
return x << ??(2);
}
Specification
Feasible sketch with
hole set to 2
Infeasible sketch; no
possible hole assignment
Introduction to Sketch
Automatically generate programs which satisfy specification given the partial program
Notes: The program synthesis tool we used for generating fast Pack-processing code is SKETCH, which originated from Prof. Armando’s phD thesis work.
The user will provide two programs: one is specification and the other one is partial program with holes in it. The goal is to find one kind of hole assignment
which guarantee that the specification program and the partial program can be semantically equivalent.
SKETCH here will use QBF solver to either fill in the hole values to make partial program become a full one if there is any feasible solutions or return false
if no possible hole assignment can satisfy semantical equivalence.
Here is a concrete example where in spec program, we obtain the return value by multipling the input value by 5. ??(2) means the one of the integer value choosing from 0 to 2^2-1
which is 3. As for the first partial program, it is feasible because SKETCH can set ??(2) to be 2 while SKETCH cannot find the satisfying result for the second partial program.
In our Chipmunk project, we will use developer’s program as the specification, use partial program to represent the structure of the substrate and use holes to represent
large but finite number of low-level hardware configurations and then use program synthesis to test its feasibility.

## Slide 5
Initialize X to random inputs
Verify hole assignment on all inputs (X ⊆ Y)
Synthesize holes that work for inputs
Hole Assignment
Counterexample Input c
Failure
Add c to X
Success
No Counterexamples
No Hole Assignment
Counterexample Guided Inductive Synthesis
Automatically generate programs which satisfy specification by providing the skeleton
Notes: SKETCH use CEGIS algorithm to do program synthesis. We call it internal cex mode.
To be specific, SKETCH divides the whole program synthesis problem into two phases: synthesis phase and verification phase.
The synthesis phase will use try to solve holes’ value assignments to satisfy the ‘partial’ inputs and the verification phase will
verify the hole value assignments on all inputs which is specified by programmers.
For example, if we set the input range to be 5 bits which is the default value of sketch. In the beginning, sketch will randomly choose
subset of all inputs to do the synthesis problem, if it fails it means there should be no feasible solutions for this partial program; if
it succeeds, it will continue to the verification stage to test more inputs. If we pass the verification, we are lucky enough to find the
final solution otherwise, there is at least one input making the current hole assignment fail to work. So we add this counterexample
Into the input set and repeat synthesis again. Back and forth until we get the final result

## Slide 6
Stateful ALU
State storage
PHV
Input
Mux
if (count == 10):
count = 0
pkt.sample = 1
else:
count++
pkt.sample = 0
Program as a packet transaction in Domino
Chipmunk
compiler
Banzai simulator for programmable switch hardware
State
Variable
Packet
Field
PHV
Container
Stateless ALU
Stateless ALU
Stateful ALU
State storage
PHV
PHV
Container
Stateless ALU
Stateless ALU
PHV
PHV
Container
Stateful ALU
State storage
Stateful ALU
State storage
Output
Mux
PHV
Container
PHV
Container
PHV
Container
Chipmunk Structure or Banzai simulator?
Notes: All our benchmarks will be borrowed from benchmarks in Domino. Just as the program shown here, each program has
both state variables and packet field. We will modify the stateful variables in Stateful ALU in Banzai simulator while change
the value of packet field in stateless ALU
The Banzai simulator model extends RMT with stateful computation, aiming at abstracting out a switch computation
Into a 2D grid of ALUs. The x axis represents pipeline stages (or we can call it depth) and the y axis represents
Parallel ALUs within a particular pipeline (or we can call it width). All packet fields values are stored in PHV (packet header vectors)
and all ALUs’ computations are atomic so that the next packet arriving at that ALU a clock cycle later will see the updated value
for stateful variables.

## Slide 7
Stateful ALU and Stateless ALU
state_0
pkt_0, pkt_1
if (rel_op(Opt(state_0), Mux3(pkt_0, pkt_1, C()))) {
state_0 = Opt(state_0) + Mux3(pkt_0, pkt_1, C());
}
include "muxes.sk";
include "rel_ops.sk";
include "constants.sk";
StateResult atom_template(int state_1, int state_2, int pkt_1, int pkt_2, int pkt_3, int pkt_4, int pkt_5) {
if (rel_op(Opt(state_1), Mux3(pkt_1, pkt_2, C()))) {
state_1 = Opt(state_1) + Mux3(pkt_1, pkt_2, C());
}
StateResult ret = new StateResult();
ret.result_state_1 = state_1;
ret.result_state_2 = state_2;
return ret;
}

## Slide 8
Stateful ALU and Stateless ALU
// Max value of opcode is 5
int {{ alu_name }}({{arg_list|join(',')}}, int opcode_hole_local, int immediate_operand_hole_local, int mux1_ctrl_hole_local, int mux2_ctrl_hole_local, int mux3_ctrl_hole_local) {
int opcode = opcode_hole_local;
int immediate_operand = immediate_operand_hole_local;
int x = {{ mux1 }}({{potential_operands|join(',')}}, mux1_ctrl_hole_local);
int y = {{ mux2 }}({{potential_operands|join(',')}}, mux2_ctrl_hole_local);
int z = {{ mux3 }}({{potential_operands|join(',')}}, mux3_ctrl_hole_local);
if (opcode == 0) {
return immediate_operand;
} else if (opcode == 1) {
return x + y;
} else if (opcode == 2) {
return x + immediate_operand;
} else if (opcode == 3) {
return x - y;
} else if (opcode == 4) {
return x - immediate_operand;
} else {
return immediate_operand - x;
}
}
Manually create the stateless ALU to support arith operator,

## Slide 9
Optimization methods to speed up synthesis
Reduce the constant values
External counterexample mode vs hole-elimination mode
Canonicalized allocation vs synthesized allocation
Gradual search for stateless ALU

## Slide 10
Reduce the constant values
#define FREEZE_TIME 10
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}
#define FREEZE_TIME 2
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}
Constrain all constants appear in benchmarks into 2-bit range in order to reduce the search space of program synthesis

## Slide 11
Input Spec file
Sketch Compiler
Failure – Counter Example c Found
Add c to X
Verification on 10 bits
Completed Sketch File
Successful Verification
Completes spec with 2 bit inputs
Verified Sketch File
Input Sketch file
External counterexample mode vs hole-elimination mode
NOTE: this figure is borrowed from NSDI, we should make a lot of changes
Do verification in 10-bit range
Add the counterexample into input if the verification fails
Constrain the input into 2-bit range for synthesis

## Slide 12
Container 1
Container 2
Container 3
Container 4
Container 1
Container 2
Container 3
Container 4
Field 1
Field 2
Field 3
Field 4
Field 1
Field 2
Field 3
Field 4
Indicator-variable allocation
Canonical allocation
Canonicalized allocation vs synthesized allocation
Synthesized-allocation and Canonicalized-allocation are “semantically” equivalent
Canonicalized-allocation has smaller search space for program synthesis problem
Synthesized-allocation and Canonicalized-allocation are “syntatically” different

## Slide 13
Gradual search for stateless ALU
Stateless alu
Stateless_alu_arith_rel_cond
Stateless_alu_arith_rel
Stateless_alu_arith
NOTE: It looks like we delete the table to compare compilation time of stateless_alu vs stateless_alu_arith
in HotNets paper. We could add them back to the paper if there is enough space (7 pages at most)
and then show the table/graph here

## Slide 14
Benchmark introduction
Add (1==1)
Switch the if-else statement
Switch the order of statement within if
Totally three ways to generate mutator
if (condition_1) {do A;} else {do B;} -----> if(!condition_1) {do B;} else {do A;}
if (condition_1 && condition_2) -----> if (condition_2 && condition_1)
if (condition_1) {do A;} -----> if (condition_1 && 1==1) {do A;}
Manually create some ”noise” for program so as to increase compilation difficult for traditional Domino compiler

## Slide 15
Compilation result
Compilation result
Resource usage
Compilation time
Compare Chipmunk with Domino in three aspects

## Slide 16
Program | Chipmunk | Domino | Compilation time (sec)
RCP | 100% | 100% | 17.7
Stateful Firewall | 100% | 90% | 2295
Sampling | 100% | 0% | 7.3
BLUE (increase) | 100% | 0% | 10.7
BLUE (decrease) | 100% | 0% | 10.7
Flowlet switching | 70% (timeout) | 100% | 52.5
Detecting new flows | 100% | 0% | 3648
Detecting flow reordering | 100% | 0% | 7.78.3
Compilation result
Compilation time

## Slide 17
Program | Chipmunk | Domino
RCP |  | 
Stateful Firewall |  | 
Flowlet switching |  | 
Resource usage

## Slide 18
Compilation result
In general, Chipmunk can compile many mutation that Domino cannot
However, due to the complexity of program synthesis problem, the compilation time of Chipmunk is much longer than Domino
Chipmunk will find the optimal resources usage, with smaller depth and width
NOTE: How should we explain the width issue?

## Slide 19
Future direction
Improve the degree of completeness of compilation result
Fill in ‘hot’ holes region to speed up synthesis time
Synthesize network programs with bounded inaccuracy over a packet trace