## Slide 2
Background: Hard to write fast code for programmable substrates

## Slide 3
Solution: Use program synthesis to autogenerate fast code

## Slide 4
int spec(int x) {
return x*5;
}
int sketch1(int x) implements spec {
return x << ??(2) + x;
}
int sketch2(int x) implements spec {
return x << ??(2);
}
Specification
Feasible sketch with
hole set to 2
Infeasible sketch; no
possible hole assignment
Introduction to Sketch

## Slide 5
Initialize X to random inputs
Verify hole assignment on all inputs (X ⊆ Y)
Synthesize holes that work for inputs
Hole Assignment
Counterexample Input c
Failure
Add c to X
Success
No Counterexamples
No Hole Assignment
Counterexample Guided Inductive Synthesis

## Slide 6
Stateful ALU
State storage
PHV
Input
Mux
if (count == 10):
count = 0
pkt.sample = 1
else:
count++
pkt.sample = 0
Program as a packet transaction in Domino
Chipmunk
compiler
Banzai simulator for programmable switch hardware
State
Variable
Packet
Field
PHV
Container
Stateless ALU
Stateless ALU
Stateful ALU
State storage
PHV
PHV
Container
Stateless ALU
Stateless ALU
PHV
PHV
Container
Stateful ALU
State storage
Stateful ALU
State storage
Output
Mux
PHV
Container
PHV
Container
PHV
Container
Chipmunk Structure or Banzai simulator?
Notes: Replace triangle with trapezoid in mux.

## Slide 7
Stateful ALU and Stateless ALU

## Slide 8
Optimization methods to speed up synthesis
Reduce the constant values
External counterexample mode vs hole-elimination mode
Canonicalized allocation vs synthesized allocation

## Slide 9
Reduce the constant values
#define FREEZE_TIME 10
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}
#define FREEZE_TIME 2
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}

## Slide 10
External counterexample mode vs hole-elimination mode

## Slide 11
Container 1
Container 2
Container 3
Container 4
Container 1
Container 2
Container 3
Container 4
Field 1
Field 2
Field 3
Field 4
Field 1
Field 2
Field 3
Field 4
Indicator-variable allocation
Canonical allocation
Canonicalized allocation vs synthesized allocation

## Slide 12
Benchmark introduction
Add (1==1)
Switch the if-else statement
Switch the order of statement within if
Totally three ways to generate mutator
if (condition_1) {do A;} else {do B;} -----> if(!condition_1) {do B;} else {do A;}
if (condition_1 && condition_2) -----> if (condition_2 && condition_1)
if (condition_1) {do A;} -----> if (condition_1 && 1==1) {do A;}

## Slide 13
Compilation result
Compilation result
Resource usage
Compilation time
Compare Chipmunk with Domino in three aspects

## Slide 14
Program | Chipmunk | Domino | Compilation time (sec)
RCP | 100% | 100% | 17.7
Stateful Firewall | 100% | 90% | 2295
Sampling | 100% | 0% | 7.3
BLUE (increase) | 100% | 0% | 10.7
BLUE (decrease) | 100% | 0% | 10.7
Flowlet switching | 70% (timeout) | 100% | 52.5
Detecting new flows | 100% | 0% | 3648
Detecting flow reordering | 100% | 0% | 7.78.3
Compilation result
Compilation time

## Slide 15
Program | Chipmunk | Domino
RCP |  | 
Stateful Firewall |  | 
Flowlet switching |  | 
Resource usage

## Slide 16
Future direction
Improve the degree of completeness of compilation result
Fill in ‘hot’ holes region to speed up synthesis time
Synthesize network programs with bounded inaccuracy over a packet trace