## Slide 1: Autogenerating fast packet-processing code using program synthesis
Xiangyu Gao, Taegyun Kim, Aatish Kishan Varma, Anirudh Sivaraman, Srinivas Narayana
Notes: I am Xiangyu, I am a first-year PhD student in New York University.
Today, I will present our work in developing a code generator Chipmunk which automatically generates fast packet-processing code using program synthesis. This is joint work with Taegyun, Aatish and Anirudh from NYU and Srinivas from Rutgers.

## Slide 2: Programming network devices today
Lots of programmable network devices (e.g., …) TODO: Add pictures.
Easy to get started with programming these devices, but hard to write optimized code.
Notes: Recently, there has been a popularity of programmable network substrates. For example, high-speed programmable switch, multicore SoC SmartNICs, FPGAs software middleboxes and the networking stack within servers. Compared with fixed devices, always come with between 10 to 100x performance loss relative to a line-rate one. With growing link speed, there is need to run ever faster packet-processing code on these substrates.
However, even though these substrates become programmable, designing and developing fast programs for them is difficult mainly for two reasons.
First, developing such fast programs requires manual optimization by experts who are familiar with each underlying hardware architecture. For example they should be aware of the cache and memory hierarchy for CPUs and SoC-based NICs; ALU, TCAM and SRAM limit for programmable switches; lookup tables, placement and routing for an FPGA etc.

## Slide 3: Programming network devices today
Lots of programmable network devices (e.g., …) TODO: Add pictures.
Easy to get started with programming these devices, but hard to write optimized code.
Because of two main reasons:
Notes: Recently, there has been a popularity of programmable network substrates. For example, high-speed programmable switch, multicore SoC SmartNICs, FPGAs software middleboxes and the networking stack within servers. Compared with fixed devices, always come with between 10 to 100x performance loss relative to a line-rate one. With growing link speed, there is need to run ever faster packet-processing code on these substrates.
However, even though these substrates become programmable, designing and developing fast programs for them is difficult mainly for two reasons.
First, developing such fast programs requires manual optimization by experts who are familiar with each underlying hardware architecture. For example they should be aware of the cache and memory hierarchy for CPUs and SoC-based NICs; ALU, TCAM and SRAM limit for programmable switches; lookup tables, placement and routing for an FPGA etc.

## Slide 4: Why developing fast programs hard?
Requires familiarity with the underlying hardware architecture
Code generation using an optimized compiler. But, engineering an optimized compiler takes a long time.
Notes: So with this emphasis on using programmable substrates and writing fast packet-processing code in them, let’s look at the difficulty to develop fast programs. There are two main reasons for this. First of all, developing such fast programs requires manual optimization by experts who are familiar with each underlying hardware architecture. For example, they must be aware of the cache and memory hierarchy for CPUs and SoC-based NICs; ALU, TCAM and SRAM limits for programmable switches; and of lookup tables, placement and routing for an FPGA. In reality, Microsoft hired a dedicated team of hardware engineers to program its FPGA-based SmartNIC.
Then, you may ask the question: why no design an optimizing compiler to reduce the workload for manual optimization but do optimization automatically. This brings the second reason. I agree that an optimizing compiler will definitely alleviate the difficulties of generating such fast code, but building the optimizing compiler itself is arduous but fruitless because the building step requires significant engineering efforts, usually it will span decades, which is both time-consuming and money-consuming and cannot catch up with the evolving network hardware. Neither academic and industrial area have strong motivation to do this development.
Therefore, in response to the above concerns, we look at this problem in another aspect and try to use program synthesis to develop code generators for emerging network substrates.

## Slide 5
Solution: Use program synthesis to generate code
Notes: So in response to the above concerns, here comes to the primary contribution to this talk: introducing program synthesis to develop code generator which we can use to generate fast packet-processing code. In other words, we map the code generation problem to one program synthesis problem and make full use of the existing program synthesis tools to solve the problem automatically.
I will talk about the details in the later slides.

## Slide 6: Classical solution to optimized code
But, engineering an optimized compiler takes a long time.
Solution: Use program synthesis to build code generators for programmable network devices
Requires familiarity with the underlying hardware architecture
Code generation using an optimized compiler
Notes: Then, you may ask why not design an optimizing compiler to do this stuff automatically? This turns to the second reason. I agree that an optimizing compiler will definitely alleviate the difficulties of generating such fast code, but the process of building one optimizing compiler itself will take quite long time which may not be available for new and evolving network hardware.
Therefore, in response to the above concerns, we look at this problem in another aspect and try to use program synthesis to develop code generators for emerging network substrates.

## Slide 7: Why program synthesis for code generation?
Small programs
But lot of value in generating highly optimized code
Programs don’t change that often, so long synthesis times are not as much of a concern.
Notes: Obviously, program synthesis problem face a key challenge: it will take quite a long time to solve it because it is a search problem over a large combinatorial search space of programs and the space grows exponentially with the number of bits in the hardware configurations. However, it is still meaningful to use it here mainly because of three reasons.
First of all, most fast packet-processing programs are naturally small and simple (because they only need to support very easy algorithms in programmable deices), and if we use powerful machines and run our job in parallel, we can find the solution within reasonable time.
Second, we currently there are more and more mature open-source synthesis tools and promising real-world applications of synthesis. We can forsee the appearance of new and well-developed synthesis tools which can speeding up the problem largely.
The third one is closely related to the real life situation.

## Slide 8
Introduction to Program Synthesis
Automatically construct a program that satisfy given specification.
Notes: Program synthesis is to automatically construct a program that satisfy given specification. Specification can be set of input/output examples (unit tests), natural language, first order logic expression or any other form that is easier to write the expected program. The early 21st century has seen a surge of practical interest in the idea of program synthesis in the formal verification community and related fields.
Since 2014 there has been a yearly program synthesis competition comparing different algorithms for program synthesis in a competitive event, the Syntax-Guided Synthesis Competition (or SyGuS-Comp). SyGus constrains the search space programs using syntactic restrictions. As a concrete example of syntax-guided synthesis, SKETCH, a programmer provides a program synthesizer the specification along a sketch. Just as the example show here, the partial program with holes representing values within a finite range of integers, which can be used to encode the programmer’s insight into the structure of the implementation, ALU functionality in programmable switch to be specific. The synthesizer completes the sketch by filling in all holes with concrete values so that the completed sketch meets the specification, where given an input range the performance of completed sketch should be exactly the same as the specified program or semantically equivalent, or says that synthesis is infeasible.

## Slide 9
int spec(int x) {
return x*5;
}
int sketch1(int x) implements spec {
return x << ??(2) + x;
}
int sketch2(int x) implements spec {
return x << ??(2);
}
Specification
Feasible sketch with
hole set to 2
Infeasible sketch; no
possible hole assignment
Introduction to Sketch
Automatically generate programs which satisfy specification given the partial program
Notes: The program synthesis tool we used for generating fast Pack-processing code is SKETCH, which originated from Prof. Armando’s phD thesis work.
The user will provide two programs: one is specification and the other one is partial program with holes in it. The goal is to find one kind of hole assignment which guarantee that the specification program and the partial program can be semantically equivalent within the input range we give. SKETCH here will either fill in the hole values to make partial program become a full one if there is any feasible solutions or return false if no possible hole assignment can satisfy semantic equivalence.
The concrete example is one spec program, we obtain the return value by multipling the input value by 5. ??(2) means the one of the integer values choosing from 0 to 2^2-1which is 3. As for the first partial program, it is feasible because SKETCH can set ??(2) to be 2 while SKETCH cannot find the satisfying result for the second partial program.
Similar to the example show here, the partial program with holes representing values within a finite range of integers, which can be used to encode the programmer’s insight into the structure of the implementation, ALU functionality in programmable switch to be specific. In our Chipmunk project, we will use developer’s program as the specification, use partial program to represent the structure of the substrate and use holes to represent large but finite number of low-level hardware configurations and then use program synthesis to test its feasibility.

## Slide 10
Initialize X to random inputs
Verify hole assignment on all inputs (X ⊆ Y)
Synthesize holes that work for inputs
Hole Assignment
Counterexample Input c
Failure
Add c to X
Success
No Counterexamples
No Hole Assignment
Counterexample Guided Inductive Synthesis
Automatically generate programs which satisfy specification by providing the skeleton
Notes: This slide shows the operational mechanism by SKETCH. SKETCH use CEGIS algorithm to do program synthesis, here we call it internal cex mode for simplicity.
The program synthesis problem solves for hole values in the formula in first-order logic which is a QBF (quantified boolean formula) problem which is harder than SAT problem. Apart from that, there is no QBF solvers which are optimized for program synthesis. Therefore, SKETCH uses CEGIS method to divide the whole program synthesis problem into two phases: synthesis phase and verification phase to reduce the computation complexity.
The synthesis phase will use try to solve holes’ value assignments to satisfy the ‘partial’ inputs and the verification phase will verify the hole value assignments on all inputs which is specified by programmers. For example, if we set the input range to be 5 bits which is the default value of sketch. In the beginning, sketch will randomly choose subset of all inputs to do the synthesis problem, if it fails it means there should be no feasible solutions for this partial program; if it succeeds, it will continue to the verification stage to test more inputs. If we pass the verification, we are lucky enough to find the final solution otherwise, there is at least one input making the current hole assignment fail to work. So we add this counterexample into the input set and repeat synthesis again. Back and forth until we get the final result.
Both synthesis and verification of CEGIS are simpler than directly solve the QBF problem because for each step we either fix test inputs or hole values which turns the QBF problem into a SAT problem which can be fed to a more efficient SAT solver.

## Slide 11
Stateful ALU
State storage
PHV
Input
Mux
if (count == 10):
count = 0
pkt.sample = 1
else:
count++
pkt.sample = 0
Program as a packet transaction in Domino
Chipmunk
compiler
Banzai simulator for programmable switch hardware
State
Variable
Packet
Field
PHV
Container
Stateless ALU
Stateless ALU
Stateful ALU
State storage
PHV
PHV
Container
Stateless ALU
Stateless ALU
PHV
PHV
Container
Stateful ALU
State storage
Stateful ALU
State storage
Output
Mux
PHV
Container
PHV
Container
PHV
Container
Chipmunk Structure or PISA simulator
State variable  Stateful ALU; Packet field  Stateless ALU
Abstract out a switch computation flow into a 2D grid of ALU
Notes: All our benchmarks will be borrowed from benchmarks in Domino. Just as the program shown here, each program has
both state variables and packet field. We will modify the stateful variables in Stateful ALU in Banzai simulator while change
the value of packet field in stateless ALU
The Banzai simulator model extends RMT with stateful computation, aiming at abstracting out a switch computation
Into a 2D grid of ALUs. The x axis represents pipeline stages (or we can call it depth) and the y axis represents
Parallel ALUs within a particular pipeline (or we can call it width). All packet fields values are stored in PHV (packet header vectors)
and all ALUs’ computations are atomic so that the next packet arriving at that ALU a clock cycle later will see the updated value
for stateful variables.

## Slide 12
Stateful ALU and Stateless ALU
state_0
pkt_0, pkt_1
if (rel_op(Opt(state_0), Mux3(pkt_0, pkt_1, C()))) {
state_0 = Opt(state_0) + Mux3(pkt_0, pkt_1, C());
}
include "muxes.sk";
include "rel_ops.sk";
include "constants.sk";
StateResult atom_template(int state_1, int state_2, int pkt_1, int pkt_2, int pkt_3, int pkt_4, int pkt_5) {
if (rel_op(Opt(state_1), Mux3(pkt_1, pkt_2, C()))) {
state_1 = Opt(state_1) + Mux3(pkt_1, pkt_2, C());
}
StateResult ret = new StateResult();
ret.result_state_1 = state_1;
ret.result_state_2 = state_2;
return ret;
}

## Slide 13
Stateful ALU and Stateless ALU
// Max value of opcode is 5
int {{ alu_name }}({{arg_list|join(',')}}, int opcode_hole_local, int immediate_operand_hole_local, int mux1_ctrl_hole_local, int mux2_ctrl_hole_local, int mux3_ctrl_hole_local) {
int opcode = opcode_hole_local;
int immediate_operand = immediate_operand_hole_local;
int x = {{ mux1 }}({{potential_operands|join(',')}}, mux1_ctrl_hole_local);
int y = {{ mux2 }}({{potential_operands|join(',')}}, mux2_ctrl_hole_local);
int z = {{ mux3 }}({{potential_operands|join(',')}}, mux3_ctrl_hole_local);
if (opcode == 0) {
return immediate_operand;
} else if (opcode == 1) {
return x + y;
} else if (opcode == 2) {
return x + immediate_operand;
} else if (opcode == 3) {
return x - y;
} else if (opcode == 4) {
return x - immediate_operand;
} else {
return immediate_operand - x;
}
}
Manually create the stateless ALU to support arith operator,

## Slide 14
Optimization methods to speed up synthesis
Reduce the constant values
External counterexample mode vs hole-elimination mode
Canonicalized allocation vs synthesized allocation
Gradual search for stateless ALU
Notes: Chipmunk can beat Domino in almost every aspects at the sacrifice of compilation time. Because the program synthesis problem is a QBF problem
whose total time increases exponentially as the number of holes increase. For example, if there are n holes, then the search space will be as large as 2^n
and most of our benchmarks generate 200 holes.
Therefore, we come up with four main ideas listed above to speed up synthesis problem. Later, I will discuss them one by one.

## Slide 15
Reduce the constant values
#define FREEZE_TIME 10
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}
#define FREEZE_TIME 2
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}
Constrain all constants appear in benchmarks into 2-bit range in order to reduce the search space of program synthesis
Notes: The first part is to reduce the constant values appearing in benchmarks.
For example, the example shown in the slides is blue_decrease.c in Domino program. We manually scan the program and downgrade all constants
appearing in program into constants within 2-bit range. Here, we replace 10 by 2.
The benefit of this transformation is that all constant/immediate holes appear in Chipmunk will only be 2-bit range which can dramatically reduce the
total number of holes. Although we slightly change the semantics of some of benchmarks, but for these case, we only focus on the compilation result
so this change is reasonable.
In future work, we will try to add constant synthesis algorithm to avoid semantic modification.

## Slide 16
Input Spec file
Sketch Compiler
Failure – Counter Example c Found
Add c to X
Verification on 10 bits
Completed Sketch File
Successful Verification
Completes spec with 2 bit inputs
Verified Sketch File
Input Sketch file
External counterexample mode vs hole-elimination mode
NOTE: this figure is borrowed from NSDI, we should make a lot of changes
Do verification in 10-bit range
Add the counterexample into input if the verification fails
Constrain the input into 2-bit range for synthesis
Z3
Notes: Previously, we introduce the CEGIS algorithm implemented in SKETCH. We call that internal counterexample mode program synthesis mode.
We referred from that idea to develop our own version of CEGIS, we call it external counterexample mode. Instead of throwing the whole
synthesis problem with 10-bit input into sketch, we divide into two parts: synthesis & verification in 2-bit input; -> verification in 10-bit inputs
-> if failed then add the counterexample in synthesis part so the synthesis step will be all 2-bit input + counterexample; else we are lucky
enough to find a sol in smaller input range which satisfies 10-bit input

## Slide 17
Container 1
Container 2
Container 3
Container 4
Container 1
Container 2
Container 3
Container 4
Field 1
Field 2
Field 3
Field 4
Field 1
Field 2
Field 3
Field 4
Indicator-variable allocation
Canonical allocation
Canonicalized allocation vs synthesized allocation
Synthesized-allocation and Canonicalized-allocation are “semantically” equivalent
Canonicalized-allocation has smaller search space for program synthesis problem
Synthesized-allocation and Canonicalized-allocation are “syntatically” different
Notes: In addition to modification in original program and our “own” external counterexample mode,
we want to add more constrain which not only conserves the function of Chipmunk but also
reduce the search space.
In allocation case, we found that all possible position on the LHS can be mapped to one particular
way in the RHS, so there must be some benefit if we choose to remove the freedom to force
packet field to specific container.

## Slide 18
Gradual search for stateless ALU
Stateless alu
Stateless_alu_arith_rel_cond
Stateless_alu_arith_rel
Stateless_alu_arith
NOTE: It looks like we delete the table to compare compilation time of stateless_alu vs stateless_alu_arith
in HotNets paper. We could add them back to the paper if there is enough space (7 pages at most)
and then show the table/graph here
Notes: For some benchmarks, there are only some of the simple operation in packet fields, so we can
choose simpler stateless ALU so that the total hole numbers can get slighted decreased. But there
are still some disadvantages if we use simplied version of stateless ALU because it may convert
from success to failure.
If permitted, we can make full use of the distributed system to run different stateless ALUs
In different machine and use optimal result. (fail from full stateless ALU or success from simplified stateless ALU)

## Slide 19
Benchmark introduction
Add (1==1)
Switch the if-else statement
Switch the order of statement within if
Totally three ways to generate mutator
if (condition_1) {do A;} else {do B;} -----> if(!condition_1) {do B;} else {do A;}
if (condition_1 && condition_2) -----> if (condition_2 && condition_1)
if (condition_1) {do A;} -----> if (condition_1 && 1==1) {do A;}
Manually create some ”noise” for program so as to increase compilation difficult for traditional Domino compiler
Notes: For benchmarks, we started with eight programs drawn from multiple sources and these programs were previously compiled with Domino. Then, we mutated these programs in semantic-preserving ways to generate 10 mutations of each of the 8 programs. The way we generate mutations is based on the following ‘noise generation’ method, adding one obviously true condition in if statement, switch the if-else statement and switch the order of statement within if. The mutation generator will pass the program several times and add some ‘semantically equivalent modifications’ to the program. In theory, if Domino can generate code for original program successfully, it should do so for ten mutations. However, this is not the case.

## Slide 20
Compilation result
Compilation result
Resource usage
Compilation time
Compare Chipmunk with Domino in three aspects
Notes: Our current experiment results have shown the advantages of our Chipmunk mainly in two aspects. For completeness, although we can not guarantee that Chipmunk has 100% completeness for generating code but its performance has already much better than Domino.

## Slide 21
Program | Chipmunk | Domino | Compilation time (sec)
RCP | 100% | 100% | 17.7
Stateful Firewall | 100% | 90% | 2295
Sampling | 100% | 0% | 7.3
BLUE (increase) | 100% | 0% | 10.7
BLUE (decrease) | 100% | 0% | 52.5
Flowlet switching | 70% (timeout) | 100% | 3648
Detecting new flows | 100% | 0% | 7.7
Detecting flow reordering | 100% | 0% | 8.3
Compilation result
Compilation time
Notes: Domino fails to generate code for most mutations of the original programs because it incorrectly concludes that the programs are too expressive to be implemented, which is avoided in Chipmunk because it reaches 100% for most of them which should be expected. After all, we can find a way to generate code for original programs. As for some programs which is rejected by Chipmunk are all because they reach the timeout we set for them (30 min per iteration).
If we provide enough time, they will finally provide the successful compilation result because we manually plug in hole values generate by other benchmarks and run verification on it, it generate the result.
Note: add the graph to show why theoratically, Chipmunk should work for every mutator
Note:

## Slide 22
Program | Chipmunk | Domino
RCP |  | 
Stateful Firewall |  | 
Flowlet switching |  | 
Resource usage
Notes: Even for mutations both Domino and Chipmunk are successful, Chipmunk can generate code with fewer pipeline stages which is severely constrained in programmable switches (12 for Tofino). The reason that in some cases Chipmunk may consume more ALUs per stage is because sometimes, if we expand the pipeline to more stages, we can balance computation task to future stages and reduce the number of ALUs used per stage. But given the priority of number of pipeline stages, we prefer to use Chipmunk.

## Slide 23
Compilation result
In general, Chipmunk can compile many mutation that Domino cannot
However, due to the complexity of program synthesis problem, the compilation time of Chipmunk is much longer than Domino
Chipmunk will find the optimal resources usage, with smaller depth and width
NOTE: How should we explain the width issue?
Notes: Emphasize the conclusion again and reiterate the benefit of Chipmunk and show why its result will be much better.

## Slide 24
Future direction
Improve the degree of completeness of compilation result
Fill in ‘hot’ holes region to speed up synthesis time
Synthesize network programs with bounded inaccuracy over a packet trace
Notes: The initial experiment results look promising however we think this is still a beginning for this project. Throughout the whole process, we also develop many future directions worthwhile for further research. Here, I want to list the three most important ones for more open discussion. As for further speeding up, can we reduce the program synthesis time by replacing hot code regions with fast implementations using a database of localized code rewrite? As for realistic simulation, in addition to the program itself, how should we address other resource constraints like memory usage which depends on the workload? As for more usage in real programmable substrates, for example, can we generate code that runs on multi-core SmartNIC platforms?

## Slide 25
Conclusion
Notes: To conclude, Chipmunk makes full use of program synthesis ideas to automatically generate fast packet-processing code which is more complete and hardware-resource saving at the cost of long compilation time. The current results encourage us to do more further research including speeding up synthesis time and implement this idea to more programmable substrates. I am welcoming for all feedback. Thank you.