## Slide 1: Autogenerating fast packet-processing code using program synthesis
Xiangyu Gao, Taegyun Kim, Aatish Kishan Varma, Anirudh Sivaraman, Srinivas Narayana
Notes: I am Xiangyu, I am a first-year PhD student in New York University.
Today, I will present our work in generating fast packet-processing code using program synthesis. This is joint work with Taegyun, Aatish and Anirudh from NYU and Srinivas from Rutgers. .
Change the logo of NYU

## Slide 2: Programmable network devices today
Lots of programmable network devices (e.g., switches, SmartNICs, NetFPGA)
Easy to get started with programming these devices
But hard to write fast packet-processing code that fits within resource constraints.
40 – 100 Gbits/s
6.5 Tbits/s
40 Gbits/s
Notes: Recently, programmable network substrates have become more and more popular because they are more flexible than fixed-function devices.
This is also the main reason why people want to use them to gradually replace the traditional fixed ones.
In addition to programmability, with the growing link speeds, there is a need to speed up the running time in programmable substrates by using faster packet-processing code. For example, SmartNICs run at line rates of 40-100 Gbit/s. Switches run at 100Gbit/s per port, a few Tbit/s in aggregate.
To be specific, in the background where various network algorithms(i.e Congestion control algo; load balancing algorithms) appear so quickly, “Researchers and engineers need to try out thousands of ideas” and hence they have more requirements for low-level
network. However, traditional fixed network substrates have fixed functionality and users cannot fundamentally change it. If the designers want to include more functions into fixed substrates, it may take several years.
However, developing fast programs in programmable substrates is really difficult.
Change the smartNIC picture

## Slide 3: Today’s approach to writing fast programs
Handcraft the fast programs
  Requires familiarity with the underlying hardware architecture
Rely on the compiler.
  Engineering a compiler takes a long time and teams of many people (e.g., large compiler teams at Intel/AMD/ARM).
  Hard to find such teams for new, niche, and evolving packet-processing hardware.
Arithmetic logic unit (ALU)
Lookup Table
Cache and memory hierarchy
Notes: There are two main reasons. First of all, developing such fast programs requires manual optimization by experts who are familiar with each underlying hardware architecture. For example, they must be aware of the cache and memory hierarchy for CPUs and SoC-based NICs; ALU, TCAM and SRAM limits for programmable switches; and of lookup tables, placement and routing for an FPGA. In reality, Microsoft hired a dedicated team of hardware engineers to program its FPGA-based SmartNIC.
Then, you may ask the question: why not design an optimizing compiler to reduce the workload and do optimization automatically. This brings the second reason. I agree that an optimizing compiler will definitely alleviate the difficulties of generating such fast code, but building the optimizing compiler itself is arduous but hard to make progress because the building step requires significant engineering efforts, usually it will span decades, which is both time-consuming and money-consuming and cannot catch up with the evolving network hardware. Neither academic nor industrial area have strong motivation to do this.

## Slide 4
Proposal: Program synthesis for code generation
Program synthesis: Auto-generate a program from a specification
Search space of Implementation candidates
Specification
Exhaustive
Search
Algorithm
Implementation
that satisfies specification
Summary: Use program synthesis as an enabling technology for building compilers for programmable network devices.
Notes: So in response to the above concerns, here comes to the primary contribution in this talk: introducing program synthesis to develop code generator which we can use to generate fast packet-processing code.
In other words, we map the code generation problem to one program synthesis problem and make full use of the existing program synthesis tools to solve it automatically.
Program synthesis is to automatically construct a program that satisfy given specification. Specification can be set of input/output examples (unit tests), natural language, or any other form that is easier to write the expected program. The user will provide a specification and a family of implementation candidates and then the program synthesis machine will implement search algorithm to find the implementation that satisfies specification. Because of its automatic code generation ability, people call it the “Ultimate Dream of CS”
I will talk about the details in the later slides.

## Slide 5: Why use synthesis for code generation?
For fast packet processing, there is value to generating high-quality code on some metric using exhaustive search based on synthesis:
  Pipelined architectures: Latency
  Processor architectures: Throughput
  Pipeline: Memory/power consumption
Synthesis can discover good assembly implementations with lower engineering effort relative to handcrafted rules for translating user programs into machine code.

## Slide 6: But, synthesis can be very time consuming
The challenge: search space might be very large.
But, can leverage domain structure in packet processing:
  Small and simple programs
  Packet-processing programs don’t change that often
And improvements in synthesis technology
  Many mature open-source synthesis tools
  Synthesis benchmarks and competitions
Notes: Of course, program synthesis problem face a key challenge: it will take quite a long time to solve it because its a search space grows exponentially where the final result hides in a small area of the search space. However, it is still meaningful to use it here mainly because of three reasons.
First of all, most fast packet-processing programs are naturally small and simple (because they only need to support very easy algorithms in programmable devices), and if we use powerful machines and run our job in parallel, we can find the solution within reasonable time. It may be impossible for us to find a needle in Pacific Ocean with only one diver but if we have 1000 divers and ask them to pick up a needle in NYU swimming pool, they may finish it within an hour
The second one is closely related to the real life situation. Programs don’t change that often, so long synthesis times are not as much of a concern because usually the frequency of code generation is low.
In addition, currently there are more and more mature open-source synthesis tools and promising real-world applications of synthesis. We can foresee the appearance of new and well-developed synthesis tools which can speeding up the problem.
The early 21st century has seen a surge of practical interest in the idea of program synthesis in the formal verification community.
Since 2014 there has been a yearly program synthesis competition comparing different algorithms for program synthesis in a competitive event, the Syntax-Guided Synthesis Competition (or SyGuS-Comp).
So every year, we get more synthesis tools candidates through the competition.

## Slide 7
Feasible partial program
Infeasible partial program;
no hole assignment
int spec(int x) {
return x + x + x;
}
Specification
int sketch1(int x) implements spec {
return x * ??;
}
int sketch2(int x) implements spec {
return x + ??;
}
Tutorial on the SKETCH program synthesizer
int sketch1(int x) implements spec {
return x * 3;
}
Notes: The program synthesis tool we used for generating fast Pack-processing code is SKETCH.
The user will provide two programs: one is specification and the other one is partial program with holes in it. The goal is to find one kind of hole assignment which guarantee that the specification program and the partial program can be semantically equivalent within the input range we give. SKETCH here will either fill in the hole values to make partial program become a full one if there is any feasible solutions or return false if no possible hole assignment can satisfy semantic equivalence.
For a concrete example, if we want to obtain the return value of multiplying the input value by 5. Here ??(2) means the one of the integer values within 2 bits. As for the first partial program, it is feasible because SKETCH can set ??(2) to be 2 while SKETCH cannot find the satisfying result for the second partial program.
Just a hint, the partial program with holes representing values within a finite range of integers can be used to encode the programmer’s insight into the structure of the programmable substrates.
Hole definition, Cite the sketch paper in the right corner
Use SKETCH to represent program synthesis engine; use sketch to represent partial program that is fed to the program synthesis engine.

## Slide 8
Verify hole assignment on all inputs (X ⊆ Y)
Synthesize holes that work for inputs
Hole Assignment
Counterexample Input c
Failure
Add c to X
Success
No Counterexamples
No Hole Assignment
Initialize X to random inputs
SKETCH’s synthesis algorithm
Counterexample Guided Inductive Synthesis
Notes: This slide shows the operational mechanism by SKETCH. SKETCH use CEGIS algorithm to do program synthesis.
The program synthesis problem solves for hole values in the formula in first-order logic which is a QBF (quantified Boolean formula) problem which is harder than SAT problem. Therefore, CEGIS divides the whole program synthesis problem into two phases: synthesis phase and verification phase.
The synthesis phase will use try to solve holes’ value assignments to satisfy the ‘partial’ inputs and the verification phase will verify the hole value assignments on all inputs which is specified by programmers. For example, if we set the input range to be 5 bits. In the beginning, sketch will randoml
y choose subset of all inputs to do the synthesis, if it fails it means there should be no feasible solutions; if it succeeds, it will continue to the verification stage to test more inputs. If we pass the verification, we are lucky enough to find the final solution otherwise, there is at least one input making the current hole assignment fail to work. So we add this counterexample into the input set and repeat synthesis again. Back and forth until we get the final result.
Both synthesis and verification of CEGIS are simpler than directly solve the QBF problem because for each step we either fix test inputs or hole values, turning the QBF problem into a SAT problem which can be fed to a more efficient SAT solver.

## Slide 9: Using SKETCH for code generation
Programmer’s program
(SKETCH specification)
©
Partial program representing
Hardware capabilities
SKETCH program synthesis
engine
Completed program output
by SKETCH
Compiler developer
Programmer
Compiler
Low-level machine code

## Slide 10
if (count == 10):
count = 0
pkt.sample = 1
else:
count++
pkt.sample = 0
Program as a packet transaction in Domino
State
Variable
Packet
Field
Stateful ALU
State storage
PHV
Input
Mux
Partial program for PISA simulator
PHV
Container
Stateless ALU
Stateless ALU
Stateful ALU
State storage
PHV
PHV
Container
Stateless ALU
Stateless ALU
PHV
PHV
Container
Stateful ALU
State storage
Stateful ALU
State storage
Output
Mux
PHV
Container
PHV
Container
PHV
Container
Case study: Using SKETCH for switch code generation
Chipmunk
compiler
Machine code for PISA simulator
Notes: In our Chipmunk project, we will use developer’s program as the specification, use partial program to represent the structure of the substrate and use holes to represent large but finite number of low-level hardware configurations and then use program synthesis to test its feasibility.
All our benchmarks are borrowed from Domino. Just as the program shown here, each program has
both state variables and packet field. We will modify the stateful variables in Stateful ALU while change
the value of packet field in stateless ALU.
The simulator model extends RMT with stateful computation, aiming at abstracting out a switch computation
Into a 2D grid of ALUs. The x axis represents pipeline stages (or we can call it depth) and the y axis represents
Parallel ALUs within a particular stage (or we can call it width). All packet fields values are stored in PHV (packet header vectors)
and all ALUs’ computations are atomic so that the next packet arriving at that ALU a clock cycle later will see the updated value.
Mention that transactions have transactional semantics.
Add the animation and introduce Domino

## Slide 11: Hardware configurations as SKETCH holes
Stateful ALU
State storage
PHV
Input
Mux
PHV
Container
Stateless ALU
Stateless ALU
PHV
PHV
Container
Stateful ALU
State storage
Stateful ALU
State storage
Stateless ALU
Stateless ALU
Stateful ALU
State storage
PHV
Container
PHV
PHV
Container
PHV
Container
PHV
Container
Output
Mux
Output Mux
Input Mux
Constant value
Immediate value
Stateful active
Stateless opcode
Notes: We have so many holes even within a very simple example. We have input Mux to control which value should be fed to one particular stage; we have output mux to determine the value passed to the next stage; we have constant value and immediate value to decide the constants used in stateless and stateful ALU; we have stateful active to monitor which stateful ALU is responsible for modifying the stateful value and we also have stateless opcode to represent the functionality of stateless ALU

## Slide 12: Evaluation: What should the baseline be?
P4-14/P4-16 compilers from chip vendors (e.g., Barefoot, Netronome, Xilinx)?
  Don’t support the (relatively) high-level atomic/transactional programming model supported by Domino.
Open source p4c compiler?
  Supports software packet processing targets that have a different architecture
So, we compare Chipmunk against Domino’s existing compiler
  Uses handcrafted rules for translating Domino programs to simulator machine code

## Slide 13: Evaluation: What benchmarks should we use?
Picked benchmark programs from Domino paper.
However, these programs were all written to ensure successful Domino compilation.
Question: if we mutate these programs in semantic-preserving ways, will Domino still compile them?
  Theoretically, yes: if a program compiles, an equivalent program should also compile
  Empirically, maybe: how good are Domino’s handcrafted rules in finding machine code to implement a Domino program?
  Types of mutations: switch order of predicates in an if clasuse.
Notes: For benchmarks, we started with eight programs drawn from multiple sources and these programs were previously compiled with Domino. Then, we mutated these programs in semantic-preserving ways to generate 10 mutations for each of the 8 programs. The way we generate mutations is based on the following ‘noise generation’ method, switch the if-else statement and switch the order of statement within if. The mutation generator will pass the program several times and add some ‘semantically equivalent modifications’ to the program. In theory, if Domino can generate code for original program successfully, it should do so for ten mutations. However, this is not the case.
Get rid of the first one

## Slide 14
Program | Chipmunk | Domino | Chipmunk Compilation time (sec)
RCP | 100% | 100% | 17.7
Stateful Firewall | 100% | 90% | 2295
Sampling | 100% | 0% | 7.3
BLUE (increase) | 100% | 0% | 10.7
BLUE (decrease) | 100% | 0% | 52.5
Flowlet switching | 70% (timeout) | 100% | 3648
Detecting new flows | 100% | 0% | 7.7
Detecting flow reordering | 100% | 0% | 8.3
Evaluation: how do Domino and Chipmunk compare on the mutations?
Domino compilation time: Very quick; few seconds on most benchmarks
Notes: Our experiment results have shown the advantages of our Chipmunk mainly in two aspects.
Domino fails to generate code for most mutations of the original programs because it incorrectly concludes that the programs are too expressive to be implemented, which is avoided in Chipmunk because it reaches 100% for most of them which should be expected. Some programs which is rejected by Chipmunk are all because they reach the timeout we set for them (30 min per iteration). Here the average of compilation time for each mutations in Flowlet switching is about an hour.
If we provide enough time, they will finally provide the successful compilation result.
Note: add the graph to show why theoretically, Chipmunk should work for every mutator
Note: Make the table and font size larger

## Slide 15
Program | Chipmunk | Domino
RCP |  | 
Stateful Firewall |  | 
Flowlet switching |  | 
Evaluation: resource consumption
Notes: For mutations both Domino and Chipmunk are successful, Chipmunk can generate code with fewer pipeline stages which is severely constrained in programmable switches (i.e 12 stage for Tofino switch). The reason that in some cases Chipmunk may consume more ALUs per stage is because, if we expand the pipeline to more stages, we can balance computation task to future stages and reduce the number of ALUs used per stage. But given the priority of number of pipeline stages, we prefer to use Chipmunk.
TODO: Add error bars here.

## Slide 16
Evaluation: summary
In general, Chipmunk can compile many mutation that Domino cannot
However, the compilation time of Chipmunk is much longer than Domino.
Chipmunk consumes smaller number of stages and ALUs
Notes: In general, Chipmunk can compile many mutation that Domino cannot
Chipmunk will find the optimal resources usage, with smaller depth and width
However, due to the complexity of program synthesis problem, the compilation time of Chipmunk is much longer than Domino
Emphasize the conclusion again and reiterate the benefit of Chipmunk and show why its result will be much better.
We are currently working on heuristics to speed up Chipmunk’s compilaton time.

## Slide 17
Conclusion
Program synthesis can play an important role in code generation
Could expand to generate fast programs for more programmable substrates (e.g., SmartNIC, FPGAs, DPDK, etc.)
Notes: To conclude, Chipmunk transplants program synthesis ideas to automatically generate fast packet-processing code which is more complete and hardware-resource saving at the cost of long compilation time.
We have shown that program synthesis can play an important role in code generator
Based on the current research result, we are confident that the application of this idea can expand to generate fast programs for more programmable substrates
The research is still ongoing and I am welcoming for all feedback. Thank you for listening.

## Slide 18
Conclusion and future directions
Speed up synthesis time (e.g. use multiple machines)
Synthesize “superoptimized” code for processors
Synthesize fast but approximate packet-processing programs
Notes: The initial experiment results look promising. however we think this is still a beginning for this project. Throughout the whole process, we also develop many directions worthwhile for further research. Here, I want to list the three most important ones for open discussion.
As for further speeding up, can we reduce the program synthesis time by using multiple machine or to say our own parallel computation method? Can we try synthesize “superoptimized” code for processors? Also, can we synthesize fast but approximate packet-processing programs?
What do we mean by this? Synthesize “superoptimized” code for processors

## Slide 19
Evaluation: Mutation types
Switch the if-else statement
Switch the order of statement within if
if (condition_1) {do A;} else {do B;} -----> if(!condition_1) {do B;} else {do A;}
if (condition_1 && condition_2) -----> if (condition_2 && condition_1)
Essentially: create some ”noise” for program so as to increase compilation difficult for traditional Domino compiler

## Slide 20
Speeding up synthesis
Our own CEGIS Algorithm
Canonicalized allocation vs synthesized allocation
Gradual search for stateless ALU
Notes: Chipmunk can beat Domino in almost every aspects at the sacrifice of compilation time. Because the program synthesis problem is a QBF problem
whose total time increases exponentially as the number of holes increase. For example, if there are n holes, then the search space will be as large as 2^n
and most of our benchmarks generate 200 holes.
Therefore, we come up with three main ideas listed above to speed up synthesis problem. I will discuss them one by one.

## Slide 21
Reduce the constant values
#define FREEZE_TIME 10
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}
#define FREEZE_TIME 2
#define DELTA2 2
struct Packet {
int now;
int now_plus_free;
};
int last_update;
int p_mark;
void func(struct Packet p) {
p.now_plus_free = p.now - FREEZE_TIME;
if (p.now_plus_free > last_update) {
p_mark = p_mark - DELTA2;
last_update = p.now;
}
}
Constrain all constants appear in benchmarks into 2-bit range in order to reduce the search space of program synthesis
Notes: The first part is to reduce the constant values appearing in benchmarks.
For example, the example shown in the slides is blue_decrease.c in Domino program. We manually scan the program and downgrade all constants
appearing in program into constants within 2-bit range. Here, we replace 10 by 2.
The benefit of this transformation is that all constant/immediate holes appear in Chipmunk will only be 2-bit range which can dramatically reduce the
total number of holes. Although we slightly change the semantics of some of benchmarks, but for these case, we only focus on the compilation result
so this change is reasonable.
In future work, we will try to add constant synthesis algorithm to avoid semantic modification.

## Slide 22
Input Spec file
Sketch Compiler
Failure – Counter Example c Found
Add c to X
Verification on 10 bits
Completed Sketch File
Successful Verification
Completes spec with 2 bit inputs
Verified Sketch File
Input Sketch file
Our own CEGIS Algorithm
Do verification in 10-bit range
Add the counterexample into input if the verification fails
Constrain the input into 2-bit range for synthesis
Z3 solver
Notes: The first part is to use our own CEGIS algorithm.
Previously, we introduce the CEGIS algorithm implemented in SKETCH. We referred from that idea to develop our own version of CEGIS.
Instead of throwing the whole synthesis problem with 10-bit input into sketch, we divide into two parts: synthesis & verification in 2-bit input; -> do verification in 10-bit input range -> if the verification failed then we add the counterexample into synthesis part so the synthesis step will have all 2-bit input + counterexample we generated from all previous verification steps; otherwise we are lucky enough to find a sol in smaller input range which satisfies for all 10-bit input.

## Slide 23: Programming network devices today
Lots of programmable network devices (e.g., …) TODO: Add pictures.
Easy to get started with programming these devices, but hard to write optimized code.
Notes: And the main reason why people want to use programmable substrates to gradually replace the traditional fixed ones is that the former enjoy the function flexibility which is not shared by the later one. To be specific, in the background where various AI and IoT applications appear so quickly that people have more requirements for low-level network. However, traditional fixed network substrates have fixed functionality and users cannot fundamentally change it. If the designers want to include more functions into programmable substrates, it may take several years. In addition to programmability, with the growing link speeds, there is a need to speed up the running speed in programmable substrates by using faster packet-processing code. For example, SmartNICs run at line rates of 40-100 Gbit/s. Switches run at 100Gbit/s per port, a few Tbit/s in aggregate.
So with this emphasis on using programmable substrates and writing fast packet-processing code in them, developing fast programs is really difficult.

## Slide 24
Container 1
Container 2
Container 3
Container 4
Container 1
Container 2
Container 3
Container 4
Field 1
Field 2
Field 3
Field 4
Field 1
Field 2
Field 3
Field 4
Indicator-variable allocation
Canonical allocation
Canonicalized allocation vs synthesized allocation
Synthesized-allocation and Canonicalized-allocation are “semantically” equivalent
Canonicalized-allocation has smaller search space for program synthesis problem
Synthesized-allocation and Canonicalized-allocation are “syntatically” different
Notes: In addition to our “own” CEGIS algorithm,
we want to add more constrain which not only conserves the function of Chipmunk but also
reduce the search space.
In allocation case, we found that all possible position on the LHS can be mapped to one particular
way in the RHS, so there must be some benefit if we choose to remove the freedom by forcing
packet field to specific container.

## Slide 25
Gradual search for stateless ALU
Arithmetic
(i.e. +/-)
Relation
(i.e. !=, >, <)
Condition
(i.e. if-else)
Boolean
(i.e. ||, &&)
Rank the operation appearing in program by frequency
Choose simpler stateless ALU for program synthesis
Notes: For some benchmarks, there are only some of the simple operation in packet fields, so we can
choose simpler stateless ALU so that the total hole numbers can get slightly decreased. But there
are still some disadvantages if we use simplified version of stateless ALU because it may convert
from success to failure.
If permitted, we can make full use of the distributed system to run different stateless ALUs
In different machine and use optimal result. (fail from full stateless ALU or success from simplified stateless ALU)

## Slide 26
Stateful ALU and Stateless ALU
state_0
pkt_0, pkt_1
if (rel_op(Opt(state_0), Mux3(pkt_0, pkt_1, C()))) {
state_0 = Opt(state_0) + Mux3(pkt_0, pkt_1, C());
}
include "muxes.sk";
include "rel_ops.sk";
include "constants.sk";
StateResult atom_template(int state_1, int state_2, int pkt_1, int pkt_2, int pkt_3, int pkt_4, int pkt_5) {
if (rel_op(Opt(state_1), Mux3(pkt_1, pkt_2, C()))) {
state_1 = Opt(state_1) + Mux3(pkt_1, pkt_2, C());
}
StateResult ret = new StateResult();
ret.result_state_1 = state_1;
ret.result_state_2 = state_2;
return ret;
}

## Slide 27
Stateful ALU and Stateless ALU
// Max value of opcode is 5
int {{ alu_name }}({{arg_list|join(',')}}, int opcode_hole_local, int immediate_operand_hole_local, int mux1_ctrl_hole_local, int mux2_ctrl_hole_local, int mux3_ctrl_hole_local) {
int opcode = opcode_hole_local;
int immediate_operand = immediate_operand_hole_local;
int x = {{ mux1 }}({{potential_operands|join(',')}}, mux1_ctrl_hole_local);
int y = {{ mux2 }}({{potential_operands|join(',')}}, mux2_ctrl_hole_local);
int z = {{ mux3 }}({{potential_operands|join(',')}}, mux3_ctrl_hole_local);
if (opcode == 0) {
return immediate_operand;
} else if (opcode == 1) {
return x + y;
} else if (opcode == 2) {
return x + immediate_operand;
} else if (opcode == 3) {
return x - y;
} else if (opcode == 4) {
return x - immediate_operand;
} else {
return immediate_operand - x;
}
}
Manually create the stateless ALU to support arith operator,